## Slide 1: Urban Water Use Efficiency Objectives
Presented By
as proposed by the State Water Resources Control Board in March 2023
Notes: SIERRA

## Slide 2
Adapting to a Hotter Drier Future
Create storage space for up to 4 million acre‐feet of water
Recycle and reuse at least 800,000 acre‐feet of water per year by 2030
Support local stormwater capture projects in cities and towns with the goal to increase annual supply capacity by at least 250,000 acre‐feet by 2030 and 500,000 acre‐ feet by 2040.
Reduce annual urban water demand by at least half a million acre‐feet by 2030.
Notes: SIERRA August 2022 Administration published document called “California’s Water Supply Strategy, Adapting to a Hotter, Drier Future – calls for “Freeing up 500,000 acre-feet of water through more efficient water use and conservation, helping make up for water lost due to climate change.”

## Slide 3
Water Saving Associated with SWRCB Proposal
As Estimated by SWRCB Staff
Notes: SIERRA
Over the next 6 months, it appears that the SWRCB reflects these exact estimated savings, reflecting 500,000 MAF of savings for their proposed changes

## Slide 4
Urban Water Uses in the New Framework
What’s In and What’s Out?
Notes: SIERRA
**While CII Indoor & Outdoor Use are technically excluded, there are still BMPs that could be applicable

## Slide 5
Calculating Urban Water Use Objectives
Providers will need to meet the SUM of the standards.
Water Provider’s Unique Water Objective
Outdoor
Residential Indoor
Real Water Loss
Potable Reuse Water Bonus
If applicable
Variance
If applicable
Water Use Objective
CII Dedicated Irrigation Meter
Standard
Residential Landscape
Notes: SIERRA
For each of these types of water use, suppliers would use a formula to calculate a water budget for the supplier’s entire service area, not for individual customers.
Suppliers would need to meet the overall objective, not each individual budget.

## Slide 6
Regulation Making - Where Are We?
Standards, status of each component
Components | Draft Available (Most Recent) | Final Approved
Indoor Residential WUE Standard | Yes – 11/30/21 | Yes – 9/28/22
Water Loss Standard | Yes – 9/2/22 | Yes – 10/19/22
Outdoor Residential WUE Standard | Yes – 3/15/23 | 
WUE Standards for CII Outdoor Irrigation of Landscape Area with Dedicated Irrigation meters | Yes – 3/15/23 | 
Variances for Unique Uses of Water | Yes – 3/15/23 | 
CII Water Use Performance Measures | Yes – 3/15/23 | 
Guidelines and Methodologies for Calculating Urban Water Use Objectives | Yes – 9/29/22 | 
 | Yes | Yes – 3/21
Notes: SIERRA

## Slide 7
Terminology
BMP = Best Management Practice
CII= Commercial, Industrial, Institutional
DIM= Dedicated Irrigation Meter
EP = Effective Precipitation
ETAF= Evapotranspiration Adjustment Factor
ET0 = Reference Evapotranspiration
GPCD= Gallons Per Capita (Persons) Per Day
LEF= Landscape Efficiency Factor
MWELO= Model Water Efficiency Ordinance
SLA = Special Landscape Areas
UWUO= Urban Water Use Objective
Notes: SIERRA
ETAF= Plant Factor divided by irrigation efficiency
Irrigation Efficiency = DU∗IME​
DU = Distribution Uniformity​
IME = Irrigation Management Efficiency​

## Slide 8
Residential

## Slide 9
Residential Indoor Budget
Defined in Water Code Section 10609.4
Residential Indoor
Year | 1157 Standards - DWR/SWRCB Recommendation (GPCD)
2020-2024 | 55
2025-2029 | 47
2030 + | 42
X
X
=
No proposed changes since SB 1157 in 2022
Things to Think About:
How will this impact your recycled water programs, wastewater systems?
What do studies need to address?
Population
365
Residential Indoor Budget
Notes: SIERRA
The efficient residential indoor use budget would be calculated by multiplying the standard by the supplier’s service area population, and by the number of days in the year
Lowered in 2022 based on joint recommendations from DWR and the State Water Board (SB 1157)

## Slide 10
No proposed changes since SB 1157 in 2022
Residential Landscape
Calculating Residential Outdoor Budget
Residential Outdoor Standard
Landscape Efficiency Factor
Landscape Area
Sq. Ft. of Irrigable + Irrigated Area
Net Eto
Reference Eto-Effective annual precipitation
0.62
Conversion Factor
Residential Outdoor Budget
Notes: SIERRA
Each supplier’s efficient residential outdoor water use budget would be calculated by multiplying the standard by net evapotranspiration, by the square footage of residential irrigable irrigated landscape area, and by a conversion factor of 0.62
The square footage of residential irrigable irrigated landscape area, reference evapotranspiration, and effective precipitation values will be provided by DWR, unless a supplier has produced alternative data that are, in terms of quality and accuracy, demonstrably equal or superior to what has been provided by DWR.
Net evapotranspiration (Net ETo) is equal to reference evapotranspiration (ETo) minus effective precipitation (EP).
Reference evapotranspiration (ETo) is a standard measurement of environmental parameters that affect the water use of plants.
ETo is expressed in inches per year and is an estimate of the evapotranspiration of a large field of four- to seven-inch tall, cool-season grass that is well watered. It varies from year-to-year and throughout the state1.
Effective precipitation (EP) is the portion of total precipitation that becomes available for plant growth. It too varies from year-to-year and throughout the state
Consistent with DWR’s recommendation, effective precipitation would be modeled effective precipitation using Cal-SIMETAW, a daily soil-water balance model, and capped at 25% of total precipitation.

## Slide 11
Year | Standard | INI Buffer
2020 | 0.80 | Up to 20%
2030 | 0.63 | Up to 20%
2035 | 0.55 | Up to 20%
Special Landscape Areas | 1.00 | NA
Residential Outdoor Budget
Outdoor
Water suppliers would need to demonstrate need for INI Buffer
Year | Standard | INI Buffer
Any | 0.55 | NA
Landscapes associated with new construction
Existing Landscapes
Residential SLAs include areas irrigated with recycled water.
Notes: SIERRA
The standard is a Landscape Efficiency Factor
The lower the standard, the less supplier-delivered water would be budgeted for outdoor use.
The LEF is a factor used to indicate the amount of water a supplier may need to deliver to maintain healthy and efficient landscapes across the supplier’s service area. A higher LEF value would correspond to higher water-using, less efficiently irrigated landscapes; a lower LEF value would correspond to lower water-using, more efficiently irrigated landscapes. Under the State Water Board staff proposal, the long-term standard (2035 and onwards) for residential outdoor water use would be an LEF of 55%
ETF lowered from 0.63 to 0.55 (Landscape Efficiency Factor or LEF of 55%) beginning Oct. 1, 2035.
No automatic 20% buffer for Irrigable-Not-Irrigated (INI) landscape area. Rather, up to 20% of INI can be factored into the residential outdoor water budget only “if the supplier demonstrates that those INI areas have come under irrigation”. This differs from the Department’s recommendation that the INI buffer be automatically included.
Residential Special Landscape Areas (SLAs) will be granted an ETF of 1.0 for use in calculating the residential outdoor water budget. This includes residential SLAs irrigated with recycled water. Areas planted with non-functional turf are not considered SLAs.
Irrigable Irrigated (II) landscape areas include healthy vegetation, somewhat unhealthy vegetation (e.g., brown lawns), and non-vegetative features, such as the rows between irrigated trees and features on or between vegetated areas (e.g., mulch, rocks, gravel, or weed blocking fabric; patches of bare earth; cars, trampolines, or other movable objects). ·Irrigable Not Irrigated (INI) landscape area includes very unhealthy vegetation (e.g., brown or leafless plants) and areas that are not currently being irrigated, but were irrigated in the past or may be irrigated in the future. ·Not Irrigated (NI) areas refer to residential landscapes that are not being irrigated and are unlikely to be in the foreseeable future (e.g., undeveloped or less developed areas; or hardscapes that cannot grow plants or hold water).
In its recommendations to the State Water Board, DWR proposed that the residential outdoor standard be applied to all Irrigable Irrigated areas and 20 percent of Irrigable Not Irrigated area in a supplier’s service area. DWR refers to the 20 percent of INI as an “INI buffer.” Under the proposed regulation, a supplier would calculate their residential outdoor water use budget by applying the standard to Irrigable Irrigated area, plus up to 20 percent of the INI buffer, if the supplier demonstrates those INI areas have come under irrigation. This differs from the Department’s recommendation that the INI buffer be automatically included.

## Slide 12
Defining Residential Special Landscape Areas
Outdoor
Special Landscape Areas
Notes: SIERRA
Residential Special Landscape Areas (SLAs) will be granted an ETF of 1.0 for use in calculating the residential outdoor water budget. This includes residential SLAs irrigated with recycled water. Areas planted with non-functional turf are not considered SLAs.

## Slide 13
Calculating ETAF/LEF on a micro scale
Plant | Plant Factor | Irrigation | Irrigation Efficiency | ETAF
Big tooth maple | 0.5 | Pressure compensating drip | 0.8 | 0.5/0.8 = 0.625
Valley Oak | 0.1 | Pressure compensating drip | 0.8 | 0.1/0.8 = 0.125
Fine-finger Fern | 0.7 | Lawn sprinklers | 0.52 | 0.7/0.52 = 1.35
Outdoor
Notes: SIERRA

## Slide 14
Landscape Factors
SWRCB Assumptions
Outdoor
Notes: SIERRA
Evapotranspiration Adjustment Factor= Plant Factor/Irrigation Efficiency

## Slide 15
Commercial
Notes: MICHELLE

## Slide 16
CII Performance Measures
Classification
Best Practices
Mixed Use Meters Conversion
Notes: MICHELLE
What is a BMP
They ignored our recommendations for CII BMPs
Performance measures do not include process water.
“Process water” means water used by industrial water users for producing a product or product content or water used for research and development. Process water includes, but is not limited to, continuous manufacturing processes, and water used for testing, cleaning, and maintaining equipment. Water used to cool machinery or buildings used in the manufacturing process or necessary to maintain product quality or chemical characteristics for product manufacturing or control rooms, data centers, laboratories, clean rooms, and other industrial facility units that are integral to the manufacturing or research and development process is process water. Water used in the manufacturing process that is necessary for complying with local, state, and federal health and safety laws, and is not incidental water, is process water. Process water does not mean incidental water uses.

## Slide 17
CII - Classification
SWRCB Proposal
EnergyStar Portfolio Manager (ESPM)
18 Categories
DWR Recommendation-
19 Categories
Notes: MICHELLE
CII Classification would utilize 18 categories from the U.S. EPA’s ENERGYSTAR Portfolio Manger tool.
CII Classification from DWR is 19 categories

## Slide 18
CII – Classification, cont
Notes: MICHELLE
https://www.energystar.gov/buildings/benchmark/understand_metrics/property_types#Education

## Slide 19
CII – Best Practices
Disclosable Buildings
  Defined by the CEC regulation
  Follow ENERGY STAR’s Portfolio Manager Tool
Multiple steps needed:
  Identify building owners
  Collect 12 months water use
  Provide building owners with water use data in an ESPM format
Notes: MICHELLE
Suppliers would be required to offer best management practices (BMPs) to their CII customers that meet specific criteria.
a. For customers that own or manage a building that is considered a “disclosable building” under the California Energy Commission’s “Benchmarking” regulation (Cal. Code Regs., tit. 20, § 1681, subd. (d)), the supplier would be required provide annual water use data in a format compatible with ENERGYSTAR’s Portfolio Manager tool.
b. For customers that the supplier has determined to be in the top 20 percent of water use, excluding process water, relative to other customers within their specific CII classification category (e.g., lodging), the supplier would design and implement a conservation program that includes at least one BMP (e.g., educational bill inserts) from five discrete BMP categories (e.g., Outreach, Education, and Technical Assistance). The proposed regulation specifies the BMPs categories and the specific BMPs within each category.
c. For customers the supplier has determined to be in the top 2.5 percent of water use, excluding process water, relative to all its CII customers, the supplier would design and implement a conservation program that includes at least two BMPs from each of the BMP categories.

## Slide 20
CII – Best Practices, cont.
Top 20% threshold per classification category (excluding process water)
  1 BMP per five BMP categories
Top 2.5% threshold
  2 BMPs per five BMP categories
Types of BMPS pr DWR Recommendations
Planning and assessment BMPs
  Water Assessments/Water Audits
  Water Management Plans
Water use specific actions and equipment BMPs
  Landscapes
  Incentives
  Operational Practices
Educational and cultural BMPs
  Outreach
  Technical Assistance
  Collaboration and Coordination
Notes: MICHELLE
Suppliers must provide water usage for “ disclosable buildings” (per the CEC’s “Benchmarking” regulation) in a format compatible with ENERGYSTAR Portfolio Manager tool.
Design and implement a conservation program with at least one BMP for the top 20% of water users (excluding process water) per classification category.
Design and implement a conservation program with at least two BMPs for the top 2.5% of all CII water users (excluding process water).

## Slide 21
CII Performance Measures –
Mixed Use Meters
Threshold to determine which CII landscapes qualify for conversion to DIM
  500,000 gallons annually
  Properties impacted 72,033
    DWR Recommendation was 1 acre
    Properties impacted 85,571
Defining "in-lieu" technologies
  Hardware, software, actions
CII Dedicated Irrigation Meter
Notes: MICHELLE
Dedicated irrigation meters (DIMs) or in-lieu technologies should be installed/employed for CII customers without a DIM and when the supplier estimates usage of 500 thousand gallons of water or more annually.
Suppliers would be required to install DIMs on or employ in-lieu technologies for the landscapes of CII customers that a) do not have a DIM and b) the supplier estimates using 500 million gallons of water or more annually.

## Slide 22
CII with DIMs
All CII-DIM landscapes must be measured by 2028.
  DWR currently working on CII-LAM-LUCD
Starting in 2028, suppliers will calculate their CII outdoor water budgets for those accounts with DIMs
CII SLAs exclude areas planted with non-functional turf.
CII Dedicated Irrigation Meter
Year | Standard
Through Sept. 30, 2030 | 0.80
Oct. 1, 2030 – Sept. 30, 2035 | 0.63
Oct. 1, 2035 onward | 0.45
Notes: MICHELLE
ETF lowered from 0.63 to 0.45 (LEF of 45%) beginning Oct. 1, 2035.
Under the proposed regulation, suppliers will make annual progress in measuring the irrigated area of CII landscapes with Dedicated Irrigation Meters (DIMs), with all subject landscapes being measured by 2028. For landscapes they have not measured, Suppliers will continue to report “landscape irrigation” water associated with CII landscapes with DIMs to the State Water Board via the already-required electronic Annual Report (eAR). Starting in 2028, suppliers would use the standard to calculate efficient water use budgets for CII landscapes with DIMs.
Department of Water Resources (DWR) is partnering with NV5 Geospatial (NV5G) to develop landscape measurement datasets for commercial, industrial, and institutional (CII) parcels.
ETF lowered from 0.63 to 0.45 (LEF of 45%) beginning Oct. 1, 2035.
All CII-DIM landscapes must be measured by 2028.
Starting in 2028, suppliers will calculate their CII outdoor water budgets for those accounts with DIMs.
CII SLAs exclude areas planted with non-functional turf. In addition to Model Water Efficient Landscape Ordinance (MWELO) SLAs, CII-DIM SLAs will also include:
  Bioengineered sloped
  Ponds for recreation or for sustaining wildlife
  Public swimming pools
  Existing plant collections
  Botanical gardens and arboretums
  Cemeteries built before 2015
DWR’s CII-LAM-LUCD study will use remote sensing and developed analytical processes to both map the detailed arrangement of irrigated features and further the landscape classification of urban retail water suppliers’ CII landscape features, including a delineation of functional and non-functional turf.
This effort will:
Provide irrigated landscape areas that will support districts mapping their dedicated irrigation meter (DIM) and CII parcels with large landscapes currently served by mixed-use meters.
Provide location-specific data (instead of parcel-level summaries) with more detailed classifications than the residential LAM.
Provide estimates of CII and residential parkway strip landscape area.
Schedule:
Portions of the mapped CII-LAM-LUCD dataset are expected to be delivered to DWR starting in the fall of 2023. The analysis of additional portions of the mapped CII-LAM-LUCD will be delivered on a monthly basis with data being released through the summer of 2026.
The data being provided:
The CII-LAM-LUCD effort for all urban retail water suppliers, including CII parkway strips, will use 2020 1-ft, 4-band imagery. This CII dataset will be different than the Residential LAM because it will provide the individual landscape feature polygons allowing water suppliers to align landscape features with mixed-use meter or dedicated meter irrigation areas or other necessary boundary conditions.
Since the residential LAM data did not include the landscape area of residential ‘parkway strips’ the CII-LAM-LUCD will also provide a landscape area for residential properties that could be irrigated by residential landowners that fall outside their property lines (parkway strips). Residential parkway strip analysis for most urban retail water suppliers will be based on 2018 LAM data except for the 20 urban retail water suppliers that were updated to the residential LAM 2020 imagery.
New and recently identified urban retail water suppliers will be provided residential LAM, CII-LAM-LUCD, and all parkway strip data based on 2020 1-ft, 4-band imagery.

## Slide 23
SLAs for CII landscapes with DIMs would be the same as defined under MWELO, with the following additional landscape types
  Bioengineered slopes;
  Ponds for recreation or for sustaining wildlife;
  Public swimming pools;
  Existing plant collections, botanical gardens, and arboretums; and
  Cemeteries built before 2015.
CII Dedicated Irrigation Meter
Defining CII DIM Special Landscape Areas
Notes: MICHELLE
For both residential areas and CII landscapes with DIMs, areas planted with nonfunctional turf would not be considered SLAs

## Slide 24
CII – Timeline
Notes: MICHELLE

## Slide 25
Other:
Water Loss
Variances
Potable Reuse
Notes: SIERRA

## Slide 26
Water Loss
Four Components to the Regulation
Individual volumetric real loss standard
Questionnaires on data quality, pressure management, asset management
Apparent loss data submission
Annual reports of breaks, repairs, and estimated water losses
Real Water Loss
Questionnaires are due in 2023
Notes: SIERRA
In 2022, a separate State Water Board regulation established system-specific standards for water losses (Cal. Code Regs., tit. 23, §§ 980-986). A supplier will calculate its annual water loss budget by multiplying its system-specific standard by the number of days in the year, and, depending on the units associated with the standard, by either the number of total service connections or the length of the distribution system, in miles (Figure 3). Suppliers that own and operate multiple systems will calculate an annual water loss budget by summing the estimated efficient water loss budgets associated with each system.

## Slide 27
Variances
Variances Added in SWRCB Staff Proposal
Variance
If applicable
Notes: SIERRA
Two additional provisions cited for:
  Urban tree health, and
  Pools, spas and other water features starting in 2030.
Different code requirements cited for water use by horses and other livestock.
Additional code requirements for water used in response to a state or local emergency, where “drought” is excluded from the eligible emergency events.
An ETF cap of 1.0 (LEF of 100%) for residential agricultural landscapes, and specific references for “crop coefficients” and “irrigation efficiencies”.
PROPOSED CHANGES: In addition to the variances recommended by DWR, the State Water Board staff proposal includes two provisions: · A provision for urban tree health. · A provision for pools, spas and other water features, starting in 2030.
For water use for horses and other livestock, the State Water Board staff proposal references existing code (e.g., Cal. Code Regs., tit. 23, § 697).
For water used in response to a state or local emergency, the State Water Board staff proposal references not just Government Code section 8558 subdivision (b), but also subdivision (c); it also excludes “drought” from the list of emergency events eligible for the variance.
For water used to irrigate residential agricultural landscapes, the State Water Board staff proposal caps the LEF at 100%; it also directs DWR and Suppliers to reference 1) crop coefficients developed by the Food and Agriculture Organization or the University of California Cooperative Extension and 2) the irrigation efficiencies developed by the University of California Agricultural and Natural Resources’ CropManage tool.
The proposed regulation would establish a process suppliers would follow to annually request approval to include additional II area beyond that calculated by DWR, SLAs, and variances. The supplier would be required to provide information quantifying and substantiating each request (e.g., demonstrating that the amount of water requested was delivered by the supplier for the requested use) and a description of efforts to prioritize water for existing trees.

## Slide 28
Bonus Incentive for Potable Reuse
Potable Reuse Water Bonus
If applicable
Notes: SIERRA
(F) Provides a bonus incentive for the amount of potable recycled water used the previous year when comparing the previous year’s water use with the urban water use objective, of up to 10 percent of the urban water use objective.
The 2018 Legislation also allows urban retail water suppliers to adjust their UWUO by adding an allowable portable reuse bonus incentive (WC §10609.20(d)). By comparing the amount of water used in the previous year with the UWUO plus the potable reuse bonus incentive, where applicable, urban retail water suppliers will be in a better position to help eliminate unnecessary use of water (WC §10609(a)).
Follow a process to annually request additional supplier calculated Irrigable-Irrigated landscapes beyond DWR landscape area measurement, SLAs and variances, including information “quantifying and substantiating each request” and a “description of efforts to prioritize water for existing trees.”
Bonus incentive for potable reuse shall be calculated using annual data and would incorporate potable reuse water loss and surface augmentation or groundwater recharge.

## Slide 29
Next Steps
Notes: SIERRA

## Slide 30
WUE Standard Timeline
Notes: SIERRA

## Slide 31
Questions to consider
How will this impact your agency?
What data is needed?
  CII measurements
  DIM and MUM identified and located
  Special landscape areas?
  Variances?
  Water Loss Questionnaires
How will you comply with CII requirements?
  Classifications
  BMPs
  Identifying top users (excluding process water)
  Reporting water use
Other things?
Notes: SIERRA

## Slide 32
Resource Cheat Sheet
SWRCB Presentation
  Slides
    https://www.waterboards.ca.gov/water_issues/programs/conservation_portal/regs/docs/2023/conservation_March_22_2023.pdf
  Recording
    https://www.youtube.com/watch?v=B-JTAUtg778
SWRCB Legislative Summary and Timeline
    https://www.waterboards.ca.gov/water_issues/programs/conservation_portal/california_statutes.html
CalWEP CII Water Use Classification and MUM Conversion System Resources
    https://calwep.org/commercial-industrial-institutional/
CalWEP Blog: What the Framework?
    https://calwep.org/the-state-board-releases-a-draft-framework-the-making-conservation-a-california-way-of-life-regulation/
DWR and SWRCB Primer on 2018 Water Conservation and Drought Planning Legislation
    https://water.ca.gov/News/Blog/2018/Nov-18/DWR-and-State-Water-Board-Release-Primer-on-2018-Water-Conservation-and-Drought-Planning-Legislation
SWRCB Rulemaking https://www.waterboards.ca.gov/water_issues/programs/conservation_portal/regs/water_efficiency_legislation.html
Draft Staff Framework for the Making Conservation a California Way of Life Regulation (Proposed Regulatory Framework)
    https://www.waterboards.ca.gov/board_info/agendas/2023/mar/032223_7_summary_of_reg_framework.pdf
Recommendations to SWRCB Memo
    https://water.ca.gov/-/media/DWR-Website/Web-Pages/Programs/Water-Use-And-Efficiency/2018-Water-Conservation-Legislation/RecommendationsSummary-Final-Memo-9-29-22.pdf
Water Loss Performance Standards
    https://www.waterboards.ca.gov/conservation/docs/2022/water-loss-regulatory-text-10-14-22.docx
Urban Water Use Efficiency Standards, Variances and Performance Measures
    https://water.ca.gov/Programs/Water-Use-And-Efficiency/2018-Water-Conservation-Legislation/Urban-Water-Use-Efficiency-Standards-Variances-and-Performance-Measures
Water Use Objective Exploration Tool
    https://www.waterboards.ca.gov/water_issues/programs/conservation_portal/regs/objective-exploration.html
Notes: SIERRA

## Slide 33
Thank you!
Michelle Maddaus
  Michelle@MaddausWater.com
Sierra Orr
  Sierra@MaddausWater.com